## Slide 1
DSP-PROJECT
CNN Based Audio Classification Using Mel-Spectrogram
01/13
Students : Chaitanya Ponnana
Rahul Adithya P
Surya Gurajapu

## Slide 2
IIT Bhubaneshwar
02/13
Overview of Our Approach
  Raw audio signals are high-dimensional, vary in length, and are hard for models to learn directly, so the goal is to convert each audio clip into a compact and informative time-frequency representation and then classify it into one of the selected sound classes using a CNN.
  MFCC-style processing is a common method used to convert speech or audio into useful features.
  This process includes pre-emphasis, framing, windowing, FFT, Mel filter banks, log compression, DCT, and normalization.

## Slide 3
IIT Bhubaneshwar
03/13
PIPELINE

## Slide 4
IIT Bhubaneshwar
04/13
Data Input and Audio Preprocessing
  Load dataset from CSV (train.csv)
  Select top 5 classes
  Limit to ≤ 100 samples per class (balancing)
  Load audio using librosa.
  Resample to 16 kHz.
    Fix duration to one second and Pad if short.
    Trim if long.

## Slide 5
  ,
IIT Bhubaneshwar
05/13
  Pre-emphasis: Boosts high-frequency components to balance spectral energy distribution.
  Framing: Segments signal into short-time frames assuming local stationarity.
  Windowing (Hamming): Reduces spectral leakage by smoothing frame edges.
  FFT: Transforms time-domain frames into frequency-domain representation.
MFCC Extraction Details

## Slide 6
  ,
IIT Bhubaneshwar
06/13
  Power Spectrum: Computes energy distribution across frequency bins.
  Mel Filter Bank: Maps frequencies onto the perceptual Mel scale, emphasizing human hearing.
MFCC Extraction Details
  A single number representing the total energy in that Mel frequency band

## Slide 7
  ,
IIT Bhubaneshwar
07/13
  Log Compression: Reduces dynamic range and approximates human loudness perception.
  DCT: Decorrelates filter bank outputs to produce compact MFCC features.
MFCC Extraction Details

## Slide 8
  ,
IIT Bhubaneshwar
08/13
  MFCC Representation: Encodes spectral envelope in low-dimensional form, often visualized as a 3D time–frequency–intensity representation.
  Intensity: Represents the log-scaled energy (magnitude) of the signal in each Mel-frequency band at a given time frame.
  Frame Limiting: Standardizes temporal dimension (fixed number of frames).
  Normalization: Centers features to stabilize learning and reduce bias.
  Final Output: Structured time-frequency feature map ready for CNN input.
MFCC Extraction Details

## Slide 9
  ,
IIT Bhubaneshwar
09/13
MFCC → CNN Pipeline

## Slide 10
IIT Bhubaneshwar
10/13
CNN Model Architecture
  Convolution Blocks (×3):
  Stacked Conv2D → BatchNorm → MaxPooling layers progressively extract hierarchical patterns from MFCC maps — from low-level spectral edges to high-level acoustic features.
  Feature Compression:
  Flatten + Dropout converts 2D feature maps into a compact vector while reducing overfitting and improving generalization.
  Classification Head:
  Dense(128) → Softmax learns nonlinear decision boundaries and outputs class probabilities.
Abhaya Libre

## Slide 11
IIT Bhubaneshwar
11/13
Training Setup and metrics
  Loss function: sparse_categorical_crossentropy
  Optimizer: Adam
  Metric: accuracy
  Train-test split: 80% / 20%
  Stratified split to preserve class balance

## Slide 12
IIT Bhubaneshwar
12/13
Results
  CNN

## Slide 13
IIT Bhubaneshwar
13/13
Conclusion and reference
This project combines classical DSP and deep learning in one pipeline. The DSP stage converts raw audio into structured MFCC features, and the CNN stage learns class-specific patterns from those features. That is why the presentation should be described as “DSP-based audio feature extraction followed by CNN-based deep learning classification.” MFCCs remain a widely used and practical front end for audio tasks, even though CNNs are the final classifier here.
ref 1 : https://practicalcryptography.com/miscellaneous/machine-learning/guide-mel-frequency-cepstral-coefficients-mfccs/https://haythamfayek.com/2016/04/21/speech-processing-for-machine-
learning.htmlhttps://datagenetics.com/blog/november32012/index.html
ref2 : http://practicalcryptography.com/miscellaneous/machine-learning/guide-mel-frequency-cepstral-coefficients-mfccs/
ref3 : https://haythamfayek.com/2016/04/21/speech-processing-for-machine-learning.html
ref 4 : http://datagenetics.com/blog/november32012/index.html